## Slide 1
CAN Message and Signal Extraction Using DBC
CAN Basics
CAN (Controller Area Network) is a message-based protocol used for ECU communication in vehicles.
Communication happens using CAN frames identified by CAN ID
Actual vehicle signals are packed as bits inside CAN data.
Standard CAN frame:
DLC vs Data Length
DLC = number of bytes sent in CAN frame
Data length = actual bytes used by signals Padding
fills the remaining bytes to match DLC
Signals in CAN Data
CAN data contains multiple signals
Signal = a specific set of bits representing physical values
Signals have:
  Start bit
  Bit length
  Endianness (Little/Big)
  Scaling factor & offset
  Data (up to 8 bytes = 64 bits)
  DLC
  (0–8 bytes)
  CAN ID
  (11-bit)
Tool & DBC Used
Tool: Vector CANdb++
DBC File: opel_omega_2001.dbc
CAN Type: Classical CAN (8-byte messages)
ECUs: ABS, ESP, ECU, TCU, SAS
Example from DBC File
Message Name: ABS WheelSpeed
CAN ID: 768 (0x300)
DLC: 8 bytes
Transmitter: ABS EC
Signal Name: FrontLeftWheelSpeed
Signal Definition (DBC line)
SG_ FrontLeftWheelSpeed : 5|14@0+ (0.112,0) "km/h“
  Start Bit: 5
  Length: 14 bits
  Endianness: @0 → Big Endian (Motorola format)
  Data Type: Unsigned (+)
  Factor (Scaling): 0.112
  (Raw value × 0.112 = physical value)
  Offset: 0
  Unit: km/h
DBC File & Its Need
DBC (Database CAN) is a definition file for CAN communication
It Contains:
  Message ID & name
  DLC
  Signal names, start bit, length, scaling, units
Used by software/tools to decode CAN messages automatically
Parameter | Standard CAN | Extended CAN
ID Length | 11 bits | 29 bits
Message Count | Limited | Very Large
Network Size | Small | Large
Bit Extraction:
Selecting specific bits from CAN data using DBC-defined start bit and length to obtain the raw signal value.