## Slide 1
🔁 Continuous Listening (Blocking Read)
Flow:
Create CAN socket
Bind to can0
Enter infinite loop
Call read()
Kernel blocks process
CAN frame arrives
read() returns data
Print data
Loop again
Key Point: ➡ Socket is always waiting,
CPU is blocked inside read()
Used When :
Simple testing
Single socket
No timeout needed
⚡ Event-Based Listening (select)
Flow:
Create CAN socket
Bind to can0
Enter infinite loop
Prepare fd_set
Set timeout
Call select()
Kernel waits for CAN event
CAN frame arrives OR timeout
select() wakes process
Call read() only if ready
Process data
Loop again
Key Point: ➡ Program sleeps efficiently,
wakes only on event
Used When :
Automotive gateways
Multiple sockets
CAN + Ethernet
Low CPU usage
Real ECUs